## Slide 1: ISP Overview
Marie-anne le menn
19 May 2017
Architecture and tool

## Slide 2: S32V234: Block Diagram

## Slide 3: Image Sensor Processing
Black level correction
Exposure
White balancing
HDR
Vignetting
Debayering
RGB2YUV
Noise Filter
Format Conversion
Full processing for
up to 2x1Mpix @ 30fps!

## Slide 4: AGENDA
ISP architecture
How to program it
Current software

## Slide 5: AGENDA
Its architecture
  Image processing and ISP kernels
  ISP sub-system
  ISP graph
  Sequencer and processing pipeline
  Memory management
  IPU
How to program it
Current software

## Slide 6: Image processing and ISP kernels

## Slide 7: Principle
13
Image
Kernel
Result
1 x 0 +
2 x -1 +
3 x 0 +
13 x -1+
14 x 5 +
15 x -1+
25 x 0+
26 x -1+
27 x 0
14
14
13
12 x -1+
13 x 5 +
14 x -1+
24 x 0+
25 x -1+
26 x 0
0 x 0 +
1 x -1 +
2 x 0 +
  A matrix used for image convolution for image processing

## Slide 8: Examples: Mean
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
1/49 *
1 | 1 | . | . | 1 | 1
1 | 1 | . | . | 1 | 1
. | . | . | . | . | .
1 | 1 | . | . | 1 | 1
11
11
1/121 *

## Slide 9: ISP Kernel
Can do image convolution
De-Bayering
White balancing
RGB to YUV conversion
…
But It can do much more like:
ISP kernel is a function

## Slide 10: ISP kernel
Serialized with other ISP kernels
Kernel1
Kernel 2
Kernel 3

## Slide 11: ISP Kernel examples
Kernel1
Kernel2

## Slide 12: ISP subsystem

## Slide 13: ISP Sub-system
IPUS
=
Scalar Image Processing Unit
(one result pixel at a time)
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…

## Slide 14: ISP Sub-system
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
IPUV
=
Vector Image Processing Unit
(4 result pixels at a time)

## Slide 15: ISP Sub-system
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Execute the Kernels

## Slide 16: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Each input/output can fetch/output multiple data at the same time

## Slide 17: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
The full SRAM is 4MB
=> 1MB is optimised for the ISP

## Slide 18: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Sequencer
M0 Core

## Slide 19: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Sequencer
M0 Core
Data/ Instr. RAM

## Slide 20: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Sequencer
Crypto protected
Kernel RAM
M0 Core
Data/ Instr. RAM

## Slide 21: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Sequencer
done
start
Configuration and synchronization signals
Kernel RAM
M0 Core
Data/ Instr. RAM

## Slide 22: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Sequencer
done
start
Fast DMA
DRAM
Kernel RAM
M0 Core
Data/ Instr. RAM

## Slide 23: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Sequencer
done
start
Fast DMA
Configuration and synchronization signals
done
start
Kernel RAM
M0 Core
Data/ Instr. RAM
DRAM

## Slide 24: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Sequencer
done
start
Programmable Engines
Fast DMA
done
start
Kernel RAM
Data/ Instr. RAM
M0 Core
DRAM

## Slide 25: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Sequencer
Kernel RAM
M0 Core
Data/ Instr. RAM
done
start
Fast DMA
done
start
MIPI-CSI
Camera
DRAM

## Slide 26: ISP graph

## Slide 27: Graph
Camera Input
Buffer 1
Kernel1
Buffer 2
Kernel 2
…

## Slide 28: Graph
Camera Input
Buffer 1
Kernel1
Final SRAM Buffer
…
DRAM Buffer
FAST DMA transfer

## Slide 29: ISP Kernel examples
Kernel1
Kernel2

## Slide 30: Graph
Kernel1
Buffer 1
Buffer 2

## Slide 31: Graph
Kernel1
Buffer 1
Kernel 2
…
Buffer 3
Buffer 2
Kernel 3

## Slide 32: Graph
Buffer 1
Kernel 3
…

## Slide 33: Graph
Kernel 4
Buffer 1
Kernel 3
…
…

## Slide 34: Sequencer and processing pipeline

## Slide 35: ISP Sub-system
SRAM
SRAM controller
IPU Modules
IPUS_0
IPUS_1
IPUS_7
…
IPUV_0
IPUV_3
…
Sequencer
Kernel RAM
M0 Core
Data/ Instr. RAM
done
start
Fast DMA
done
start
MIPI-CSI
Camera
DRAM

## Slide 36: Sequencer: Block Diagram
Mapped into Host address space
Peripherals can also be controlled by Host CPU: IPUs and FastDMA
Servicing the Debug Unit for the IPUs
Sequencer code runs on the M0+ core
The sequencer executes/synchronises the ISP pipeline based on the graph description

## Slide 37: ISP Pipeline
Kernel1
Kernel2
Camera image buffer
Intermediate buffer
Final buffer

## Slide 38: ISP Pipeline
Kernel1
Kernel2
Camera image buffer
Intermediate buffer
Final buffer

## Slide 39: ISP Pipeline
Final DRAM buffer
FAST DMA transfer
Final SRAM buffer

## Slide 40: IPU

## Slide 41: Scalar Engine (IPUS)

## Slide 42: Scalar Engine (IPUS)
Input window: 3x3 or 9x1
Up to 3 Inputs:
  Ex: R, G, B

## Slide 43: Scalar Engine (IPUS)
Instruction memory
Decoding unit
No data memory (no load/store), only registers

## Slide 44: Scalar Engine (IPUS)
Working matrix
Matrix ALU (3x3 -> 3x3)

## Slide 45: Scalar Engine (IPUS)
Mask matrix: To select on which elements of the matrix the operation or accelerator should be applied to
3X3 Accelerators:
Sum, scaled, clipped
Max, median, min
Other accelerators:
Histogram
PRNG

## Slide 46: Scalar Engine (IPUS)
Up to 2 output

## Slide 47: Vector Engine (IPUV)
5x5 input windows
4-way SIMD ALU
Handles operation with:
Horizontal vectors
Vertical vectors
Scalars

## Slide 48: IPU Engines
8 x IPUS & 4 x IPUV
500MHz per Engine: 6000MHz total
Pixels are 16-bit fixed point data in signed or unsigned mode
Input and output managed by the StreamDMA engines

## Slide 49: Input Matrix: IPUS
In2 | In1 | In0
In4 | In2 | In3
In7 | In6 | In5
In8 | In7 | In6 | In5 | In4 | In3 | In2 | In1 | In0
3x3
9x1

## Slide 50: Input Matrix: IPUS
Pix 0 | Pix 1 | Pix 2 | Pix 3 | Pix 4 | Pix 5 | Pix 6 | Pix 7 | Pix 8
Pix 9 | Pix 10 | Pix 11 | Pix 12 | Pix 13 | Pix 14 | Pix 15 | Pix 16 | Pix 17
Pix 18 | Pix 19 | Pix 20 | Pix 21 | Pix 22 | Pix 23 | Pix 24 | Pix 25 | Pix 26
Pix 27 | Pix 28 | Pix 29 | Pix 30 | Pix 31 | Pix 32 | Pix 33 | Pix 34 | Pix 35
Pix 36 | Pix 37 | Pix 38 | Pix 39 | Pix 40 | Pix 41 | Pix 42 | Pix 43 | Pix 44
Pix 45 | Pix 46 | Pix 47 | Pix 48 | Pix 49 | Pix 50 | Pix 51 | Pix 52 | Pix 53
Input image
Input matrix

## Slide 51: Input Matrix: IPUS
Pix 0 | Pix 1 | Pix 2 | Pix 3 | Pix 4 | Pix 5 | Pix 6 | Pix 7 | Pix 8
Pix 9 | Pix 10 | Pix 11 | Pix 12 | Pix 13 | Pix 14 | Pix 15 | Pix 16 | Pix 17
Pix 18 | Pix 19 | Pix 20 | Pix 21 | Pix 22 | Pix 23 | Pix 24 | Pix 25 | Pix 26
Pix 27 | Pix 28 | Pix 29 | Pix 30 | Pix 31 | Pix 32 | Pix 33 | Pix 34 | Pix 35
Pix 36 | Pix 37 | Pix 38 | Pix 39 | Pix 40 | Pix 41 | Pix 42 | Pix 43 | Pix 44
Pix 45 | Pix 46 | Pix 47 | Pix 48 | Pix 49 | Pix 50 | Pix 51 | Pix 52 | Pix 53
1st Input

## Slide 52: Input Matrix: IPUS
Pix 0 | Pix 1 | Pix 2 | Pix 3 | Pix 4 | Pix 5 | Pix 6 | Pix 7 | Pix 8
Pix 9 | Pix 10 | Pix 11 | Pix 12 | Pix 13 | Pix 14 | Pix 15 | Pix 16 | Pix 17
Pix 18 | Pix 19 | Pix 20 | Pix 21 | Pix 22 | Pix 23 | Pix 24 | Pix 25 | Pix 26
Pix 27 | Pix 28 | Pix 29 | Pix 30 | Pix 31 | Pix 32 | Pix 33 | Pix 34 | Pix 35
Pix 36 | Pix 37 | Pix 38 | Pix 39 | Pix 40 | Pix 41 | Pix 42 | Pix 43 | Pix 44
Pix 45 | Pix 46 | Pix 47 | Pix 48 | Pix 49 | Pix 50 | Pix 51 | Pix 52 | Pix 53
2nd Input

## Slide 53: Input Matrix: IPUS
Pix 0 | Pix 1 | Pix 2 | Pix 3 | Pix 4 | Pix 5 | Pix 6 | Pix 7 | Pix 8
Pix 9 | Pix 10 | Pix 11 | Pix 12 | Pix 13 | Pix 14 | Pix 15 | Pix 16 | Pix 17
Pix 18 | Pix 19 | Pix 20 | Pix 21 | Pix 22 | Pix 23 | Pix 24 | Pix 25 | Pix 26
Pix 27 | Pix 28 | Pix 29 | Pix 30 | Pix 31 | Pix 32 | Pix 33 | Pix 34 | Pix 35
Pix 36 | Pix 37 | Pix 38 | Pix 39 | Pix 40 | Pix 41 | Pix 42 | Pix 43 | Pix 44
Pix 45 | Pix 46 | Pix 47 | Pix 48 | Pix 49 | Pix 50 | Pix 51 | Pix 52 | Pix 53
… 5th input

## Slide 54: Input Matrix: IPUS
Pix 0 | Pix 1 | Pix 2 | Pix 3 | Pix 4 | Pix 5 | Pix 6 | Pix 7 | Pix 8
Pix 9 | Pix 10 | Pix 11 | Pix 12 | Pix 13 | Pix 14 | Pix 15 | Pix 16 | Pix 17
Pix 18 | Pix 19 | Pix 20 | Pix 21 | Pix 22 | Pix 23 | Pix 24 | Pix 25 | Pix 26
Pix 27 | Pix 28 | Pix 29 | Pix 30 | Pix 31 | Pix 32 | Pix 33 | Pix 34 | Pix 35
Pix 36 | Pix 37 | Pix 38 | Pix 39 | Pix 40 | Pix 41 | Pix 42 | Pix 43 | Pix 44
Pix 45 | Pix 46 | Pix 47 | Pix 48 | Pix 49 | Pix 50 | Pix 51 | Pix 52 | Pix 53
1st Input of the 2nd line

## Slide 55: Input Matrix: IPUS
Pix 0 | Pix 1 | Pix 2 | Pix 3 | Pix 4 | Pix 5
Pix 9 | Pix 10 | Pix 11 | Pix 12 | Pix 13 | Pix 14
Pix 18 | Pix 19 | Pix 20 | Pix 21 | Pix 22 | Pix 23
Pix 27 | Pix 28 | Pix 29 | Pix 30 | Pix 31 | Pix 32
Pix 36 | Pix 37 | Pix 38 | Pix 39 | Pix 40 | Pix 41
Pix 45 | Pix 46 | Pix 47 | Pix 48 | Pix 49 | Pix 50
9x1 mode 3rd Input

## Slide 56: Memory management

## Slide 57: ISP Kernel
A lot of image processing steps (kernels) require multiple lines:
De-bayering
Sobel filtering
IPUs can fetch pixels from different lines

## Slide 58: Image processing kernel
13
Image
Kernel
Result
13
12 x -1+
13 x 5 +
14 x -1+
24 x 0+
25 x -1+
26 x 0
0 x 0 +
1 x -1 +
2 x 0 +

## Slide 59: Image processing kernel
Image
Kernel
Result

## Slide 60: Hardware Replacement Modes
StreamDMA has a lot of additional features:
Scaling
Multiple data format support

## Slide 61: AGENDA
Its architecture
How to program it
Current software

## Slide 62: AGENDA
Its architecture
How to program it
  Graph tool
  Kernel example
  Software Components
  Build Process
  Project structure
  Optimisations
Current software

## Slide 63: Graph tool (DEMO)

## Slide 64: Kernel example

## Slide 65: Example of 2:1 Scaling and Gaussian filter
1 | 2 | 1
2 | 4 | 2
1 | 2 | 1
x 1/16
3x3 Gaussian filter
Low pass filter

## Slide 66: Example of 2:1 Scaling and Gaussian filter
1 | 2 | 1
2 | 4 | 2
1 | 2 | 1
x 1/16
1/16 | 1/8 | 1/16
1/8 | 1/4 | 1/8
1/16 | 1/8 | 1/16
1/16 equivalent to a right shift of 4
1/8 equivalent to a right shift of 3
1/4 equivalent to a right shift of 2
4 | 3 | 4
3 | 2 | 3
4 | 3 | 4
Shift Matrix:

## Slide 67: Example of 2:1 Scaling and Gaussian filter
start_scale:
mov confalu, (0 /*unsigned*/ |
(1<<1) /*saturate*/)
mov confaddt,(0 /*w*/ |
(0<<3) /*unsigned*/ |
(5<<5) /*shift*/ |
(0x40 << 9) /* scale*/)
Code: IPU configuration
Confalu and Confaddt are core registers of the IPU

## Slide 68: Example of 2:1 Scaling and Gaussian filter
Pix 1,1 | Pix 1,2 | Pix 1,3
Pix 2,1 | Pix 2,2 | Pix 2,3
Pix 3,1 | Pix 3,2 | Pix 3,3
 |  | Pix 1,1
 |  | Pix 2,1
 |  | Pix 3,1
 | Pix 1,1 | Pix 1,2
 | Pix 2,1 | Pix 2,2
 | Pix 3,1 | Pix 3,2
  done d0,i
d0:
  done d1,i
d1:
  done d2,i
Code: Input initialisation
Input matrix
InA

## Slide 69: Example of 2:1 Scaling and Gaussian filter
1 | 0 | 1
0 | 0 | 0
1 | 0 | 1
Mask Matrix
d2:
  mov maskv,0b101000101
  mov w,4 // to w
  mset 0b010101010
  mov w,3 // to w
  mov w4,2
Code: Shifting matrix initialisation

## Slide 70: Example of 2:1 Scaling and Gaussian filter
Mask matrix

## Slide 71: Example of 2:1 Scaling and Gaussian filter
1 | 0 | 1
0 | 0 | 0
1 | 0 | 1
Mask matrix
4 | 0 | 4
0 | 0 | 0
4 | 0 | 4
Working matrix W
d2:
  mov maskv,0b101000101
  mov w,4
  mset 0b010101010
  mov w,3
  mov w4,2
Code: Shifting matrix initialisation
Matrix instruction

## Slide 72: Example of 2:1 Scaling and Gaussian filter
Working matrix W

## Slide 73: Example of 2:1 Scaling and Gaussian filter
0 | 1 | 0
1 | 0 | 1
0 | 1 | 0
Mask matrix
4 | 3 | 4
3 | 0 | 3
4 | 3 | 4
d2:
  mov maskv,0b101000101
  mov w,4
  mset 0b010101010
  mov w,3
  mov w4,2
Code: Shifting matrix initialisation
Working matrix W

## Slide 74: Example of 2:1 Scaling and Gaussian filter
4 | 3 | 4
3 | 2 | 3
4 | 3 | 4
d2:
  mov maskv,0b101000101
  mov w,4
  mset 0b010101010
  mov w,3
  mov w4,2
Code: Shifting matrix initialisation
Working matrix W
Scalar instruction
(Mask matrix does not apply)

## Slide 75: Example of 2:1 Scaling and Gaussian filter
4 | 3 | 4
3 | 2 | 3
4 | 3 | 4
Shift matrix saved in Working matrix WW
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
Mask matrix
  swp // w -> ww
  mov maskv, 0b111111111
Code: Shifting matrix initialisation
(important for future instruction)

## Slide 76: Example of 2:1 Scaling and Gaussian filter

## Slide 77: Example of 2:1 Scaling and Gaussian filter
Arithmetic-shift-right InA elements according to the coefficient in WW => result saved in W
“sum” register has the sum of all elements of the W matrix. Move that value to out0, and progress to next pixel (input, xpos, output)
loop:
  lsr w,ina,ww
  dout sum,odd,ixo
odd:
  done loop,ix
end_scale:
Code: Main Loop
Fetch new entry without creating any output: scaling of 2:1
Continue the loop
The kernel will restart from the beginning for each new line

## Slide 78: Software Components

## Slide 79: ISP Application
ARM Code
main()
Support libraries
ISP libraries
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
Compiler (AARCH64 – Linux, SA)
Final APP
ARM Application for Linux or Standalone
Device drivers
3rd party libraries

## Slide 80: ISP Application
ARM Code
main()
Support libraries
ISP libraries
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
Compiler (AARCH64 – Linux, SA)
Final APP
Modified by the user
ARM Application for Linux or Standalone
Device drivers
3rd party libraries

## Slide 81: Build Process

## Slide 82: ISP Application
ARM Application for Linux or Standalone
ARM Code
main()
ISP libraries
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
Compiler (AARCH64 – Linux, SA)
Final APP
Device drivers
Support libraries
3rd party libraries

## Slide 83: Build sequence
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
Graph defined via graph design tool
ARM Application for Linux or Standalone
ARM Code
main()
ISP libraries
Compiler (AARCH64 – Linux, SA)
Final APP
Device drivers
Support libraries
3rd party libraries

## Slide 84: Build sequence
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
Graph compiled via GDT compiler -> .h and .c output
ARM Application for Linux or Standalone
ARM Code
main()
ISP libraries
Compiler (AARCH64 – Linux, SA)
Final APP
Device drivers
Support libraries
3rd party libraries

## Slide 85: Build sequence
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
IPU Kernels defined in assembly (.s file)
ARM Application for Linux or Standalone
ARM Code
main()
ISP libraries
Compiler (AARCH64 – Linux, SA)
Final APP
Device drivers
Support libraries
3rd party libraries

## Slide 86: Build sequence
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
IPU Kernels compiled - .c and .h file output
ARM Application for Linux or Standalone
ARM Code
main()
ISP libraries
Compiler (AARCH64 – Linux, SA)
Final APP
Device drivers
Support libraries
3rd party libraries

## Slide 87: Build sequence
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
Graph compiled and wrapped to C++ - .h and .a file output
ARM Application for Linux or Standalone
ARM Code
main()
ISP libraries
Compiler (AARCH64 – Linux, SA)
Final APP
Device drivers
Support libraries
3rd party libraries

## Slide 88: Build sequence
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
ISP header is included to ARM application code.
ARM Application for Linux or Standalone
ARM Code
main()
ISP libraries
Compiler (AARCH64 – Linux, SA)
Final APP
Device drivers
Support libraries
3rd party libraries

## Slide 89: Build sequence
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
ARM Application for Linux or Standalone
ARM Code
main()
ISP libraries
Compiler (AARCH64 – Linux, SA)
Final APP
Device drivers
Support libraries
3rd party libraries
Arm application is built and linked together with all the drivers, libs etc.

## Slide 90: Build sequence
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
ARM Application for Linux or Standalone
ARM Code
main()
ISP libraries
Compiler (AARCH64 – Linux, SA)
Final APP
Device drivers
Support libraries
3rd party libraries
Final application .elfs output

## Slide 91: Project structure

## Slide 92: ISP demo
ISP demo can be found in: /s32v234_sdk/demos/isp folder
Demo can be built for stand-alone and Linux environment

## Slide 93: ISP demo
The ISP graph used by the demo is defined in the BUILD.mk file in the project folder
Then the graph can be found in the folder /s32v234_sdk/isp/graphs

## Slide 94: ISP graph
In the graph sources you can find the:
.ispgraph_diagram:
  Graph created with the graph tool
  As Many as you want
.gdt: descripton file generated by the tool and used by the gdt compiler
  Generated based on the “ispgraph_diagram” with the same name as the graph folder

## Slide 95: ISP graph
ISP
Compiler (AARCH64 – Linux, SA)
ISP Graph
IPU Kernels
IPU Compiler
GDT Compiler
Graph compiled via GDT compiler -> .h and .c output
ARM Application for Linux or Standalone
ARM Code
main()
ISP libraries
Compiler (AARCH64 – Linux, SA)
Final APP
Device drivers
Support libraries
3rd party libraries

## Slide 96: ISP Graph

## Slide 97: ISP API
Allocation DRAM buffers for FastDMA transfer
Initialise camera
Start ISP sequencer
Get the output frames of the ISP (for APEX processing, display,…)
Stop ISP sequencer
Read/Write ISP registers

## Slide 98: ISP API: Initialisation (main.cpp)
// *** Initialize SDI ***
lRes = sdi::Initialize(0);
// *** create grabber ***
sdi_grabber *lpGrabber = new(sdi_grabber);
lpGrabber->ProcessSet(gpGraph, &gGraphMetadata);
// *** prepare IOs ***
sdi_FdmaIO *lpFdma = (sdi_FdmaIO*)lpGrabber->IoGet(SEQ_OTHRIX_FDMA);
// *** allocate all the DDR buffers for the fast DMA transfers***
if (lpFdma->DdrBuffersAlloc(DDR_OUT_BUFFER_CNT) != LIB_SUCCESS) {
printf("Failed to allocate FastDMA buffers\n");
return 1;
}

## Slide 99: ISP API: Initialisation (main.cpp)
// *** prestart grabber ***
lpGrabber->PreStart();
// *** configure camera parameters ***
CamConfig();

## Slide 100: ISP API: Run time (main.cpp)
To access the latest frame
gFrameIsp = lpGrabber->FramePop(FDMA_IX_ISP_OUTPUT0);
if(gFrameIsp.mImage.mData == NULL)
{
break;
} // if pop failed
When the processing of the frame is over, the buffer needs to be released:
if(lpGrabber->FramePush(gFrameIsp) != LIB_SUCCESS)
{
break;
} // if push failed
From the file graph_name_c.h

## Slide 101: ISP API: Run time (main.cpp)
Write into IPU registers:
// black level correction
seq_setReg(CHGAIN_ENGINE, 0, 0x70, 0xa18); // GPR0 (IPUS): R
seq_setReg(CHGAIN_ENGINE, 0, 0x71, 0xa18); // GPR1 (IPUS): GR
seq_setReg(CHGAIN_ENGINE, 0, 0x72, 0xa18); // GPR2 (IPUS): GB
seq_setReg(CHGAIN_ENGINE, 0, 0x73, 0xa18); // GPR3 (IPUS): B

## Slide 102: Optimisations
Kernel assembly code
Multiple kernel ran on one IPU
Static sequencing

## Slide 103: AGENDA
Its architecture
How to program it
Current software

## Slide 104: AGENDA
Its architecture
How to program it
Current software
  ISP kernels
  AEC/AWB

## Slide 105: ISP Kernels
Functions
Black level measurement
Black level correction
Dead pixel processing
Channel Gain
L/S decompression
Input decompression
Exposure measurement
HDR
De-Bayer
Color Correction Matrix
RGB2Y
Compression
YRB to YUV
Denoise Y
Subsample UV and denoise
Edge Enhancement
Functions
Channel gain
3x3 filters
Vignetting
Global tone mapping
Histogram computation
…

## Slide 106: AEC/AWB
Only basic functions to provide example
Implemented de-flickering

## Slide 107: Questions